## Slide 2: Data extraction
Autocaffe
  Verified that “dengue-sg” has no gaps in data
  Average, maximum, minimum of temperature and rainfall aggregated from daily to weekly
    Maximum consecutive days of rainfall (> 0) within the week
    Number of rainy days (> 0) within the week
    Number of hot days (> 27.8 degC) within the week
  “population-sg” midyear average
Python
  Spatial average to 5 regions (north, northeast, west, east, central), and to sg
  Compute absolute humidity from temperature-sg-avg and relative humidity
  Use Holt-Winters method to extract trend (slope) and seasonality components [1]

## Slide 3: Feature engineering
Use dengue-sg-log as output [1]
  Gradient of 0 to -4 week dengue-sg-log
Temperature data in 4-week blocks [2]
  Use mean of temperature-avg for weeks 0, -1:-4, -5:-8, -9:-12, -13:-16, and -17:-20
    “normalized” by dividing 25
  Label temperature-avg for weeks -17:-20
    < 27.8 degC as 1 else 0
  Mean number of hot days in a week
Rainfall data in 4-week blocks [2]
  Use mean of rainfall-avg for weeks -1:-4, -5:-8, -9:-12, -13:-16, and -17:-20
  Label mean rainfall-avg for weeks -13:-16
    < 10.7 mm || > 21.4 mm as 1 else 0
  Use mean of weekly rainy days (rainfall-avg > 0) for weeks -1:-4, -5:-8, -9:-12, -13:-16, -17:-20
    High rainy days could create flush events [3]
  Use mean of max consecutive rainy days (rainfall-avg > 0) for weeks -1:-4, -5:-8, -9:-12
    A combination of high and low consecutive rainy days could create stagnant conditions
    High consecutive rainy days could also create flush events [3]
Normalized population-sg
  Mean of weeks -1:-20
dengue-sg-log [1]
  Weeks -1:-6
Absolute humidity [4]
  Cross-Correlation Analysis showed lag week = 4

## Slide 4: Data extraction (unused)
  Extrapolated missing past data for temperature-central
    Use temperature by week-of-year for the past 5 “normal-looking” years
    Find offset temperature from mean temperature of the past 5 years
    Apply offset temperature to the mean annual temperature of temperature-changi (representative) to missing years
    Scaled using IQR of temperatures in the year (avoid extreme/anomalies)